## Slide 1
  SMR용 연료취급계통,
  압력 및 방사능저감계통 용기 개발
2021. 10. 20.
비에이치아이 주식회사
Notes: To

## Slide 2: Contents
  Fuel Handling System
  2. 압력 및 방사능저감계통 (Containment Pressure & Radioactivity Suppression System) 용기

## Slide 3: Fuel Handling System
  Fuel Handling System의 기능
  Fuel handling System의 특징
  Arrangement of Fuel handling System
  Fuel Assembly
  Comparison with others Refueling Machine
  3 Step Hoist Box Assembly
  Gripper Assembly & Pneumatic Services Data
  Human Friendly Operating Technology
  Precision & Automatic Equipment
  Low Radiation Level
  Soft & Safety Drive
  Time Study Report

## Slide 4: Fuel Handling System 기능
  Fuel Handling & Refueling
Move from SFSR to FTS
  SFHM
Move from FHA
to UCA
  FTS(UCA)
  FTS(FHA)
  ICI Replacement
  Auxiliary Elevator : Support ICI and
  ICI Handling tool
· FHA : Fuel Handling Area · FTS : Fuel Transfer System · NFA : New Fuel Assembly · NFE : New Fuel Elevator
· RM : Refueling Machine · SFHM : Spent Fuel Handling Machine · UCA : Upper Containment Area · SFAR : Spent Fuel Storage Rack
NFA Receipt & Inspection
  NFE
  Auxiliary
  Platform
Refueling & FTS to Reactor Vessel
  RM

## Slide 5
Fuel Handling System의 특징
Mock up 제작 및 기술 검증 필요
System Equipment
정밀 자동화 장비이며 복합기능
특수 장비이며, 높은 기술력이 필요한 진입 장벽이 높은 장비임
SMART Fuel Handling System은 기술검증 필요
원전의 전반적인 배치와 구조 이해
시스템 설계, 정밀가공, 자동화 PGM, Hydraulic 등 다양한 기술 능력 필요
공급능력 미 확보 시 고가 구매 및 장 납기 요구됨

## Slide 6: Arrangement of Fuel Handling System
Plane View
UGS
CSB

## Slide 7: Arrangement of Fuel Handling System
Front View

## Slide 8: Fuel Assembly
Comparison with SMART & APR1400
SMART
APR1400
Upper End Fitting
SMART
APR1400
APR1400
SMART
CRA*
Fuel Assembly
Gripper
* CRA : Control Rod Assembly
Fuel Assembly
Grapple
Latching Finger
Lower End Fitting

## Slide 9
WEC
AP1000(WEC)
APR1400
SMART
Comparison with others Refueling Machine

## Slide 10: 3 Step Hoist Box Assembly
Design Concept Hoist box of Refueling Machine

## Slide 11
Gripper Assembly & Pneumatic Services Data
s

## Slide 12: Human Friendly Operating Technology
Main & Hoist Operation Screen of RM
Main Operation Screen
Hoist Operation Screen

## Slide 13: Precision & Automatic Equipment
Hoist Box Up Latch
L/Switch(Dual)
Tap view Mast Assembly without Cable Reel
L/Switch for
Mast Bumper
Mast Assembly of Refueling Machine

## Slide 14: Low Radiation Level
Dose Rates from a Spent Fuel Assembly in the Refueling Pool
  Decay : Used 72 Hour
  Design Criteria : 0.025 mSv/hr
  Check Point of Refueling Machine : Up limit
Axial Dose Rate
Evaluation Radiation Level
Description | APR1400 | SMART
Water Depth above top of active fuel | 285cm | 363cm
Water Level Dose Rate | 0.01 mSv/hr | 0.0003 mSv/hr
Max. Water Level Dose Rate | 0.016 mSv/hr | 0.0045 mSv/hr
Rate as Design Criteria | 65% | 18%
APR1400
SMART

## Slide 15: Soft & Safety Drive
Purpose : Review to avoid fuel damage according to
acceleration of Refueling Machine
Permissible axial & transverse “g” load on a fuel assembly : Max. 4.0 g
Max. acceleration in Emergency Stop during transverse drive
  0.0 ~0.5 Sec Area : 0.51 m/sec2 = 0.05 g < 4.0 g
  0.5 ~1.0 Sec Area : 0.31 m/sec2 = 0.03 g < 4.0 g
Max. acceleration in Emergency Stop during vertical drive
  Acceleration in Emergency Stop : ah = -1.73 m/sec2 = -0.18 g
  Acceleration due to Elastic Energy of wire rope: ahb= 2.45 m/sec2 = 0.25 g
  Max. acceleration in Emergency Stop during vertical drive
  : av=0.25g -(-0.18g)= 0.43 g < 4.0 g
Evaluation for Acceleration of Fuel Handling Facility

## Slide 16: Time Study Report
Description |  | Speed(m/min) |  | Travel Length(m) |  | 
 |  | High | Slow | High | Slow | Total
Hoist | Reactor | 1.8 | 0.3 | 11.3 | 1.2 | 12.5
 | Rack |  |  | 2.3 | 0.6 | 2.9
Traversing | Reactor | 5.0 | 1.0 | 0.4 | 0.6 | 1
 | Rack |  |  | 2.4 | 0.6 | 3.0
Travelling | Reactor | 5.0 | 1.0 | 10.0 | 0.6 | 10.0
 | Rack |  |  | 10.0 | 0.6 | 10.0
Description | Speed(m/min) |  | Travel Length(m) |  | 
 | High | Slow | High | Slow | Total
Hoist | 1.8 | 0.3 | 2.3 | 0.6 | 12.5
Traversing | 5.0 | 1.0 | 2.2 | 0.6 | 3.0
Travelling | 5.0 | 1.0 | 9.4 | 0.6 | 10.0
Description | RM Alone | RM with SFHM
Refueling Cycle | 46 Min/Fuel Assembly | 39 Min/Fuel Assembly
Total Refueling Time (57 Assembly x 2) | 43.7 Hour x 2 Time (1day 19.7H x 2 Time) | 37.1 Hour x 2 Time (1day13.1 H x 2 Time)
Equipment | - Refueling M/C | Refueling M/C FTS - SFHM
Operator | Min. 1 Man | Min. 2 Man
Design Features | High Risk. Complicated Machine | Low Risk Proven System
Comparison RM alone and RM with SFHM

## Slide 17: Containment Pressure & Radioactivity Suppression System (CPRSS)용기
  CPRSS Lid 란
  CPRSS 계통 및 구성 기기
  CPRSS Lid 설치 형상
  General Arrangement (Overall View)
  Structure Analysis
  Seismic Restraint Part
  Sealing Calculation
  Lift Rig
  RDP (케이블 관통부) 설계

## Slide 18: CPRSS Lid 란
  CPRSS Lid (격납건물압력및방사능저감계통 덮개)
  CPRSS 계통을 구성하는 하나의 기기로, LCA UCA(Lower Containment Area) 와 UCA(Upper Containment Area)의 경계를 이루는 구조물.
  CPRSS Lid는 원자로 상부 구조물 집합체(RHSA, Reactor Head Structure Assembly) 외부에 설치되는 CAP 방식의 격납구조물로 Refueling Pool 바닥 Flange에 조립되어, 원자로에서 발생되는 온도, 압력이 원자로 건물 내부 (UCA)로 방출되는 것을 방지하는 기능 수행.

## Slide 19: CPRSS 계통 및 구성 기기
  계통구성 기기
  CPRSS Lid
  PRL (Pressure Relief Line) & PRL-Sparger
  IRWST(In-Containment Refueling Water Storage Tank)
  RTL (Radioactive material Transport Line) & RTL-Sparger
  RRT (Radioactive material Removal Tank)
  CHRS (CPRSS Heat Removal System)
    CHX (CPRSS Heat exchanger)
    CSL (CPRSS Steam Line)
    CSL Isolation valve
    CDL (CPRSS Discharge Line)
    & CDL-Sparger
    CDL Isolation valve
    CRL (CPRSS Return Line)
    CRL Isolation valve
    ECT (Emergency Cooldown Tank)
  CPRSS (Containment Pressure & Radioactivity Suppression System) 계통
  CPRSS 계통은 LOCA(Loss of Coolant Accident) 혹은 MSLB(Main Stem Line Break) 사고가 발생시 LCA(Lower Containment Area) 지역의 증가된 온도와 압력 및 방사능을 낮추는 기능을 수행함.

## Slide 20: CPRSS Lid 설치 형상

## Slide 21: General Arrangement (Overall View)
1) Safety Class(안전등급) : 2
2) Code Class(기기등급) : MC
3) Quality Class(품질등급) : Q
4) Seismic Category(지진등급) : I
5) Applicable Design Code : KEPIC MNE 2005 with 2006, 2007, 2008, and 2009 Addenda.
6) Accident Condition (DBA, Design Basis Accident)
- 내부 온도 : Max. 230 ℃
- 외부 온도 : Max. 90 ℃
- 내부 압력 : Max. 3.5 bar(a)
- 외부 압력 : Max. 0.19 bar(a)
Finite Element of Mode

## Slide 22
General Arrangement (Overall View)
Lifting Rig
Upper Parts
Lower Parts
LID Seismic Support
RDP(Refueling Disconnection Panel)
Lower Parts Flange Anchorage including Stud Bolts
Sealing
Manway
Ladder/Platform
7
9
8
6
5
4
3
2
1

## Slide 23: Structure Analysis
Stress Intensity – Top/Bottom = 42.804 MPa
Stress Intensity - Middle = 34.014 MPa

## Slide 24: Structure Analysis
Stress Evaluation at Junction |  |  |  |  |  |  |  | Unit : MPa |  | 
Case |  | Descriptions | Node No. | S1 | S2 | S3 | Stress Intensity | Allowable Value |  | FE Result
Design & Level A | 1 | Pm < Sm | 823 | 113.99 | 18.556 | -10.183 | 124.18 | < | 145.8 | O.K.
 |  | PL < 1.5Sm | 823 | 102.25 | 1.24E-08 | -50.678 | 152.92 | < | 218.7 | O.K.
Level B Weight + Design Pressure + Reaction Load + Dynamic loads (OBE) + Design Temperature | 8 | Pm < Sm | 823 | 123.411 | 18.592 | -1.402 | 128.949 | < | 145.8 | O.K.
 |  | PL < 1.5Sm | 823 | 106.175 | 1.253 | -50.678 | 159.171 | < | 218.7 | O.K.
 | 9 | Pm < Sm | 823 | 123.725 | 18.599 | -1.422 | 129.283 | < | 145.8 | O.K.
 |  | PL < 1.5Sm | 823 | 106.462 | 1.321 | -50.678 | 159.698 | < | 218.7 | O.K.
 | 10 | Pm < Sm | 823 | 123.580 | 18.596 | -1.405 | 129.121 | < | 145.8 | O.K.
 |  | PL < 1.5Sm | 823 | 106.343 | 1.382 | -50.678 | 159.382 | < | 218.7 | O.K.
Level C Weight + Design Pressure + Reaction Load + Dynamic loads (SSE) + Design Temperature | 11 | Pm < Sm | 823 | 127.912 | 18.793 | -1.671 | 133.719 | < | 145.8 | O.K.
 |  | PL < 1.5Sm | 823 | 110.101 | 2.506 | -50.678 | 165.423 | < | 218.7 | O.K.
 | 12 | Pm < Sm | 823 | 128.539 | 18.806 | -1.710 | 134.385 | < | 145.8 | O.K.
 |  | PL < 1.5Sm | 823 | 110.673 | 2.642 | -50.678 | 166.475 | < | 218.7 | O.K.
 | 13 | Pm < Sm | 823 | 128.249 | 18.801 | -1.676 | 134.061 | < | 145.8 | O.K.
 |  | PL < 1.5Sm | 823 | 110.436 | 2.764 | -50.678 | 166.475 | < | 218.7 | O.K.
Stress Evaluation : CPRSS Lid

## Slide 25
8 Pad(), 4 Pad Bracket(), 4 Wall Bracket(), 4 Lod(), 4 Left Bracket(), Right Bracket(), 8Pin(), 16 Pin Cover(), 16 Hex Bolt() & Jam Nut()
Material
-  ~  : MDF A516-70
-  : MDF A193-B7
-  : MDF A194-2H
Lid Seismic Restraint Part
Folding Configuration of Seismic Restraint

## Slide 26: Sealing Calculation
2” 4.5 UNC / Length - 475 mm
MDF A193 Gr.B8S
Stud Bolt & Nut Martial & Size

## Slide 27: Lift Rig
Part A
Part B
Part C
Part D
Part |  | Allowable Stress (MPa) | Max. Stress (MPa)
Part A | Tensile | 157.2 | 11.1
 | Shear | 104.8 | 70.2
Part B | Tensile | 157.2 | 11.1
 | Shear | 104.8 | 70.2
Part C | Tensile | 157.2 | 16.0
 | Shear | 104.8 | 101.4
Part D | Tensile | 157.2 | 22.1
 | Shear | 104.8 | 70.2

## Slide 28: RDP (Refueling Disconnection Panel, 케이블 관통부) 설계
Upper RDP
Middle RDP
Lower RDP

## Slide 29: Thank you!