## Slide 1
2015.10.28
Development Status of
Sodium-cooled Fast Reactor(SFR)
SFR 원형로 개발 현황
소듐냉각고속로개발사업단 / 김태완

## Slide 2
Outlines
Motivation & Backgrounds
SFR Program(PGSFR)
Project Activities of PGSFR
Summary
2

## Slide 3
Motivation & Backgrounds
I
3

## Slide 4: Nuclear Power Plants in Korea
Wolsong (#1,2,3,4)
Shin-Wolsong (#1,2)
Hanul (#1,2,3,4,5,6)
Shin-Hanul (#1,2)
Gori (#1,2,3,4)
Shin-Kori (#1,2)
Shin-Kori (#3,4)
Hanbit
(#1,2,3,4,5,6)
As of Jan., 2015 (Kor. Atomic Indu. Forum)
Site
Gori
Wolsong
Hanbit
Hanul
Total
In Operation
6 (5,147)
5 (3,779)
6 (5,900)
6 (5,900)
23 (20,716)
Under
Construction
2 (2,800)
1 (1,000)
-
2 (2,800)
5 (6,600)
Total
(MW)
8 (7,947)
6 (4,779)
6 (5,900)
8 (8,700)
28 (27,316)
Plants Under Construction
OPR1000 : Shin-Wolsung (#1,2)
APR1400 : Shin-Gori (#3,4), Shin-Hanul (#1,2)
Nuclear
23.5%
Fossil Fuel
60.1%
Hydro & others
16.4%
As of 2015 (MOTIE)

## Slide 5: Spent Nuclear Fuel in Korea
700 ton/yr from 23 NPPs in Korea  ~ 14,000 ton stored (75% saturated)
75%
saturated
65%
saturated
62%
saturated
77%
saturated
12%
saturated
Stored(t)
Capacity(t)
Storing Status of Spent Nuclear Fuel (as of Dec., 2013)
Wolsong
Hanbit
Hanul
Kori
Shin-wolsong
Saturation : Habit(2024), Wolsong(20125), Hanul (2026), Kori(2028)
 Additional storing facility

## Slide 6: LWR Spent Fuel Issue in Korea
A spent fuel problem is an urgent issue in Korean nuclear industry. Korean government launched PECOS(Public Engagement Commission on Spent nuclear fuels) in 2014.
10 Recommendations
Start the operation of Final Repository in 2051
Select the site for Underground Research Lab. by 2020
Develop the technologies for storage, transportation, toxicity/volume reduction
Korean spent fuel policy is “wait and see” and will be decided based on the results of option studies.

## Slide 7: Advantages of SFR + Pyro for SNF Management
Dramatic advantages in terms of managing time, waste amounts and disposal area
Total Generation Cost
Fuel Cycle Cost
HLW Volume
(+ Spent Fuel)
Decay Heat
(after 200 y)
Activity
(after 200 y)
Uranium Consumption
TRU Loss
Size of the HLW
Repository
1
0.1
0.01
0.001
LWR
LWR + FR
FR
※ Ref : OECD/NEA Report (2006)
5
20
1
Amounts
1
100
1
Area
1000
1
Direct Disposal
After SFR+Pyro
Time
300년
30만년
100
100
Direct Disposal
After SFR+Pyro
Direct Disposal
After SFR+Pyro

## Slide 8: Who are developing SFR ?
2010
2020
2030
2040
Russia
BN600
BN800
BN1200
CFR1000
CFR600
Comm. Rx
Demo. Rx
China
France
ASTRID 600
India
MFBR100
FBR-1 &2
PFBR500
FBR-1 &2
BN600
Major nuclear countries are developing the SFR to sustain energy security or to recycle SNF.

## Slide 9
SFR Program(PGSFR)
II
9

## Slide 10: Development of SFR with Pyro Process
Final Disposal
Nuclear
Power
Plant
[Spent Nuclear Fuel]
On-site
storage
PYRO Process
SFR
High-level waste
Recycling
TRU Fuel
To solve the SNF problems, SFR is being developing combined with PYRO Process technology.

## Slide 11: Major Milestones for SFR Development in Korea
System Perfor. Test
Design Approval
Detailed Design
Prototype Reactor(PGSFR)
Conceptual Design
‘07
’11
’18
’20
’28
’26
Long-Term Development Plans for Future Reactor Systems have been approved by the KAEC on December 22, 2008.
2012: Conceptual design for PGSFR
2017: Safety Analysis Report for Design Certification(SDA)
2020: Design Certification(SDA)
2022: Construction Permission(CP)
2028: Complete PGSFR construction

## Slide 12: Organization of SFRA
Ministry of Science, ICT and Future Planning (MSIP)
Committee for Promotion of SFR Development
National Research Foundation of Korea (NRF)
NSSS Design
of PGSFR
(KAERI)
PGSFR Design Demonstration
(KAERI)
Fuel Development
(KAERI)
Component Design
(Doosan)
BOP and I&C
Design
(KEPCO-E&C)
Director
Steering Committee
Advisory Board
Executive Office
SFRA

## Slide 13: Design Features of PGSFR
Rx Type : Pool Type SFR
Heat Transport : PHTS - IHTS - SHTS
Power Output : 150 MWe
System Pressure : ~1 bar
Coolant Outlet/Inlet : 545℃,/390℃
Fuel Type : Metal(U-Zr at Beginning, U-TRU ultimately)
Cladding : FC-92 (Modified HT9)
Refueling Period : 12 Months
Emergency Cooling : Passive + Active
Decay Heat Removal : Passive + Active
Design Life : 60 y
Seismic Isolation System (Operation until Seismic Intensity ~7)

## Slide 14: Roles of PGSFR in Korea
‘20
URL
Site Selection
‘16
Interim
Storage Policy
Back-end
Policy
Final
Repository
Public Debating on Spent Fuel Management
Economy
Environmental Gain
Safety & Safe Guard
‘31
‘41
‘51
Korea is developing PGSFR(Proto-type of Gen-iv Sodium-cooled Fast Reactor) to burn Trans-uranium(TRU) retrieved from LWR spent fuel by PYRO-process.
PGSFR combined with PYRO will demonstrate the pros and cons of spent fuel recycling strategy in terms of economy, environmental gain and safety, NPT. And it will also provide a basic data for the determination of the back-end fuel cycle policy.

## Slide 15
Project Activities of PGSFR
III
15

## Slide 16: Safety Characteristics of Pool-type SFR
The high boiling point of sodium at atmospheric pressure  Large margin to coolant boiling and elimination of large LOCA-like accident concern
Excellent heat transfer properties of fuel and coolant  Especially for heat removal by natural circulation in emergency
The large thermal inertia provided by the pool-type primary system  Large heat capacity to accommodate decay heat during extended period (~24 h)
Non-corrosive characteristics of sodium relative to normal structural material  Ensure high reliability of sodium cooling components

## Slide 17: Inherent Safety of Metal Fuel
Thermal properties of metal fuel
High thermal conductivity leads to relatively low fuel temperature (~700℃) during normal operation
 Low stored energy during severe accident
Relatively low melting temperature fuel (~1250℃) compared with cladding material(~1600℃)
 Significant axial expansion of metal fuel by phase change = Negative reactivity
 Melting of fuel before melting of cladding (cladding breach after melting)
 Possible elimination of pathway to severe accident
The dispersive behavior of metal fuel in severe accident
No in-core blockage. Core pin geometry is maintained and dispersed fuel flows out through core regions  Negative reactivity

## Slide 18: Design Features of PGSFR

## Slide 19: Core Configuration of PGSFR
Main Parameters | U Equilibrium
Thermal Power [MWth] | 392.6
Coolant Temperature (inlet/outlet) [oC] | 390 / 545
Fuel Form / U-235 Enrichment [wt.%] | U-10%Zr / 19.53
Cycle Length [EFPD] | 290
Structure Material (Cladding & Reflector) | HT9M
Number of Batches (Inner/Outer Core) | 4 / 5
Active Core Height [cm] | 90.0
Fuel Pin Diameter [cm] / P/D Ratio | 0.74 / 1.14
Uranium Inventory [ton] | 7.33
Average/Peak Burnup [GWd/ton] | 66.5 / 103.9
Average Power Density [W/cm3] | 218.3

## Slide 20: Fluid System Design of PGSFR
System design concept from trade-off study to enhance plant safety and to improve economics & performance
PHTS
  Pool-type
  Two PHTS pumps
  Four IHXs
IHTS
  Two loops / two steam generators(straight tubes)
  Two mechanical pumps on cold legs
  Passive protection of IHX from SG tube failure by cold leg piping layout
DHRS: Passive (PDRC) / Active (ADRC)
Energy conversion system
  Superheated steam Rankine cycle (Main path)
  Supercritical CO2 Brayton cycle (Option)

## Slide 21: Decay Heat Removal System
Safety-grade DHR system
  Ultimate heat sink for DBA
PDRC (Passive Decay heat Removal Circuit)
  Two independent heat removal loops
  DHX, AHX, Expansion tank, Air dampers
  Use of natural circulation of Sodium & Air
  Operation
    Emergency heat rejection w/o operators’ action
ADRC (Active Decay heat Removal Circuit)
  Two independent heat removal loops
  DHX, FHX, Expansion tank, EMP, Air blower, Air dampers
  Use of forced (and/or natural) circulation of sodium & Air
  Operation
    Scheduled & Emergency operation
    50% heat removal capacity for SBO condition

## Slide 22: Mechanical Structure Design
Simple Reactor Enclosure System
    Uniform vessel Thickness
    No penetrations and no attachment on vessel
Double Vessels (Reactor Vessel and Guard Vessel)
Skirt type reactor support structure excluding weld joint with reactor vessel
Significantly reduced IHTS piping length using 9Cr-1Mo-V Steel
Seismic Isolation Design for Reactor Island (Rx Bldg, Aux Bldg andWastag/Maintenance Bldg)
ASME BVP division 5 is applied to high temperature design

## Slide 23: Buildings and Structures
Reactor Building Arrangement
  Seismic Isolation Design
  * Common base mat with auxiliary building
  * Selected HDRB(High Damping Rubber Bearing)
  * Operation until seismic intensity ~7
GA design is going on with rectangular shape of auxiliary building by KEPCO E&C

## Slide 24: DHRS Test Facility (STELLA-1)
Main Characteristics of STELLA-1
Working fluid | Liquid sodium |  | Total electric power | 2.5 MW
Total sodium inventory | ~ 18 ton |  | Heat capacity of HXs | 1.0MW
Design temperature | 600oC |  | Design pressure | 10 bar
Max. flowrate for HX test | 10 kg/s |  | Max. flowrate for Pump test | 125 kg/s
STELLA-2 Design
- Integral test facility to simulate the reactor system
- Preparing for Construction (2018)
- Basic design will be completed by 2015.

## Slide 25: International Cooperation for PGSFR Development
ANL (U.S.)
IGCAR (India)
RIAR & IPPE (Russia)
CEA (France)
· Exchange of ASTRID design
information
· Exchange of sodium test
experiences
· Irradiation test of fuel cladding
and fuel rods at test reactor
· Reactor physics test for PGSFR
core simulation
· Considering supply chain
of main components
· Joint Design of PGSFR
· Exchange of SFR Technologies
and Experiences
· Exchange of Experimental DB
· Joint R&D for SFR Safety
· MOU related to SFR Safety
· Exchange of sodium test Experiences
· Considering fuel cladding irradiation
in test Reactor
· Considering supply chain
of main components

## Slide 26
Summary
IV
26

## Slide 27: Summary
SFRA is conducting the development program of Prototype of Gen-IV SFR(PGSFR) combined with PYRO system to burn TRU retrieved from LWR spent fuel.
The PGSFR combined with metal fuel is believed to open a new horizon for the nuclear safety because of its outstanding inherent and passive safety characteristics.
The national policy of back-end fuel cycle will be decided based on the performance of PGSFR+PYRO recycling system.

## Slide 28
Thank you so much
for
your attention !