## Slide 1
대전류 사이클로트론용 Multicusp 이온원 기술 현황
Yeong Heum Yeon (Ph. D. Student)
ITAEC, Department of Energy Science, Sungkyunkwan University
School of Information and Communication Engineering
Advisor: Jong Seo Chai
jschai@skku.edu

## Slide 2
Introduction
  H- Multicusp 이온원의 역사
  Multicusp 이온원에서 H- 추출 방법
Multicusp 이온원의 구조
  영구자석 역할 및 배열 형태
  전자 추이와 플라즈마 온도
  각 전극의 역할 및 배열 형태
설계 방향 및 결론

## Slide 3
M. Bacal 이 H- 이온의 체적생성법 발견
(M. Bacal et al., Phys. Rev Lett. 42 1538)
체적생성법에 의해 두 가지 구역으로 나뉨
전자 온도 제어에 의해서 수소 음이온의 생성 비율이 결정 됨
M. Bacal
Volume Effect
1977
Year
Beam Current
< 1 mA
Volume Extraction with filter field
1983
1985
Culham
1 mA
1990
1989
Small Multisucp volume source
LBL
2 mA
TRIUMF
KEK
9 mA
12 mA
1995
TRIUMF
15 mA
TRIUMF
Cesiated
Uncesiated
1998
25 mA
1994
Culham
45 ~90 mA
KEK
Frankfurt
100 mA
Culham
20 mA
  INTRODUCTION- H- Multicusp 이온원의 역사

## Slide 4
  INTRODUCTION- H- 추출 방법
H2 (v”=0) + e- (>20 eV) H2(v ” ≥5) + e-
Electron impact excitation
H2 (v”≥5) + e- (<1 eV) H + H-
Dissociative electron attachment
(J. R. Hiskes, J. Appl. Phys. 51, 4592, (1980))
(A.P. Hickman, Phys. Rev., 3495, (1991))

## Slide 5
  INTRODUCTION- H- 추출 방법
Electron Impact Excitation Part
e(>~20 eV)
Filament side
Dissociative Electron Attachment Part
e(>1 eV)
Extraction side

## Slide 6
  INTRODUCTION- H- 추출 방법
Finding optimization energy of electron
Initial magnet design and potential of electrodes
Analysis of magnetic field
electric field
And particle trajectory
Inspection of beam
characteristics
Redesign of
structure
Final model of
Ion source
Not satisfied
Yes
For the controlling electron temperature, the magnetic field and electric field should be considered.
Inside the volume source, the magnetic field is controlled by the permanent magnet array and number.
The electric field is controlled by the electric potential of electrodes.

## Slide 7
  Multicusp 이온원의 구조

## Slide 8
  Multicusp 이온원의 구조

## Slide 9
Type 1 – The cylindrical copper chamber surrounded by 10 cusp line of SmCo permanent magnets (20 rows)
(50 mm diameter by 100 mm long)
Filament | N | S
Extraction | S | N
Filament | N | S
Extraction | S | N
N
N
N
N
S
S
S
S
The position of second row is 70 mm from the end of volume source
  Multicusp 이온원의 구조- 영구자석 역할 및 배열 형태

## Slide 10
Type 2 – The cylindrical copper chamber surrounded by 20 cusp line of SmCo permanent magnets (20 rows)
Filament | N | S
Extraction | S | N
Filament | N | S
Extraction | S | N
N
N
N
N
S
S
S
S
  Multicusp 이온원의 구조- 영구자석 역할 및 배열 형태

## Slide 11
Type 3 – The cylindrical copper chamber surrounded by 28 cusp line of SmCo permanent magnets (28 rows)
Filament | N | S
Middle | None | None
Extraction | S | N
Filament | N | S
Middle | None | None
Extraction | S | N
N
N
N
N
S
S
S
S
  Multicusp 이온원의 구조- 영구자석 역할 및 배열 형태

## Slide 12
Type 2 – The cylindrical copper chamber surrounded by 20 cusp line of SmCo permanent magnets (20 rows)
  RESULTS- Permanent magnet simulation
Filament position- 30 mm

## Slide 13
Type 2 – The cylindrical copper chamber surrounded by 20 cusp line of SmCo permanent magnets (20 rows)
  RESULTS- Permanent magnet simulation
Filter Field Position- 65 mm

## Slide 14
Extraction Position-95 mm
Type 2 – The cylindrical copper chamber surrounded by 20 cusp line of SmCo permanent magnets (20 rows)
  RESULTS- Permanent magnet simulation

## Slide 15
  RESULTS- Permanent magnet simulation
Chart: Free Field Region- Filament Position
Type1
Type2
Type3
Type4
X axis
Chart: Free Field Region- Filament Position
Y axis
Z= 30 mm

## Slide 16
  RESULTS- Permanent magnet simulation
Type1
Type2
Type3
Type4
X axis
Y axis
Z= 65 mm
Chart: Filter Position
Chart: Filter Position

## Slide 17
  RESULTS- Permanent magnet simulation
Type1
Type2
Type3
Type4
X axis
Y axis
Z= 95 mm
Chart: Extraction Position
Chart: Extraction Position

## Slide 18
Simulation of electron trajectory from the filament.
The filament was tantalum and applied the thermionic emission data.
CST –Particle Studio
Ground(Before Biasing -25 kV)
Filament- Thermionic Emission
200 eV(Discharge voltage 200V)
Filtering
Plasma Electrode (-3.5 V)
Extraction Electrode (2000 V)
  Multicusp 이온원의 구조- 전자 추이

## Slide 19
Electron Impact Excitation Part
e(>~20 eV)
Filament side
Dissociative Electron Attachment Part
e(>1 eV)
Extraction side
Radius
Transverse Position
  Multicusp 이온원의 구조- 플라즈마 온도

## Slide 20
  Multicusp 이온원의 구조- 플라즈마 온도

## Slide 21
8114
9361
  Multicusp 이온원의 구조- 플라즈마 온도

## Slide 22
  Multicusp 이온원의 구조- 플라즈마 온도

## Slide 23
  Multicusp 이온원의 구조- 플라즈마 온도

## Slide 24
  Multicusp 이온원의 구조- 각 전극의 역할 및 배열
플라즈마 Sheath region 크기 결정

## Slide 25
  설계 방향 및 결론