## Slide 1: Design and construction of pulsed magnetic mirror device
1D. O, 1S. Hwang, 2B. K. Jung, 1M. Choi, 1G. Baek, 1C. Sung
1KAIST, 2KAERI
Korean Nuclear Society Spring Meeting
Jeju, Korea, May 19, 2022
E-mail: choongkisung@kaist.ac.kr

## Slide 2
Contents
Introduction
Design of the KAIMIR system
Initial plasma operation test
Summary / Future work

## Slide 3: Introduction
Schematics of plasma confinement in mirror geometry2
The needs for magnetic mirror plasma device
Magnetic mirror geometry plasma device : Open magnetic field system / confine plasma by mirror force from the B field intensity change ()
Advantage of magnetic mirror device
  Simple geometry, construction of device / Easier accessibility of diagnostics
  Continuous operation, No current drive
Gas Dynamic Trap (GDT) : Achieved maximum Te ~ 900eV plasma generation1, in 2014
  From this result, research on the development of fusion based neutron source is actively on the way
  Mirror related studies are also ongoing in other countries ex) Wisconsin (WHAM) / China (KMAX)…
[1] Bagryansky, P. A., et al. Physical review letters 114.20 (2015)
[2] https://scfh.ru/en/papers/trap-f-o-r-fusion-/

## Slide 4: Introduction
Development purpose of KAIst MIRror plasma system (KAIMIR) device
Basic plasma physics study in magnetic mirror geometry
  Physical analysis of instability in mirror plasma system
  Wave – plasma interaction in mirror plasma system
Fusion / Industrial plasma application study
  Base research for Fusion based neutron source
  Research of industrial plasma source
  Edge plasma in fusion and divertor region physics study
Schematic of KAIMIR device
Actual photograph of KAIMIR device
Example of KAIMIR plasma discharge

## Slide 5: Design of the pulsed plasma system
Overall system
Diameter 0.65m / length 2.48m cylindrical structure, consists of Source / Center / Expander Chamber
Generate center region 0.04~0.08T / mirror region 0.2~0.4T mirror geometry B field by Solenoid / Mirror coil
Apply arc plasma gun as a source, designed for ~5ms, pulsed high density plasma generation
Drawing of KAIMIR device

## Slide 6: Design of the pulsed plasma system
Magnetic field simulation
Bz along r = 0
Mirror / Solenoid coil current : 150A / 150A in simulation
Nearly uniform at center of the chamber
0.08T at center / 0.44T at mirror nozzle → Mirror ratio ~ 5
Aims to Max. 300A current discharge to coil (150A in present)

## Slide 7: Design of the pulsed plasma system
Magnetic field measurement
Magnetic field measurement / simulation results by changing Axial location
(Gauss meter calibration factor: 0.9)
Magnetic field measurement / simulation results by changing coil current value (Location : mirror nozzle)
Apply current 10A / 10A in mirror / solenoid coil, measure B field by axial location
  Mirror region 340G / center region 65G, formation of mirror ratio ~5, B field geometry
B field measurement by changing coil current in the center of mirror coil
  Verified linear proportionality of B field intensity by current value change
Measured / simulated data agree each other in Axial location / Current value

## Slide 8: Design of the pulsed plasma system
Magnetic coil power system
Power module
Series connection of 2.7V / 2000F capacitor [60ea (Solenoid) / 80ea (mirror)] → Max. possible voltage charge : 162V (Solenoid) / 216V (mirror)
Applies power to four electromagnetic coils connected in parallel
Steady magnetic field generation after ~0.1s
Time evolution of Coil V / I / B field (solenoid coil, 10V, 0.5s pulse, measured center of the coil)

## Slide 9: Design of the pulsed plasma system
Piezo-electric
valve
Plasma gun
Source chamber
Center
chamber
Expander
PFN
Cathode
Cath-anode
Collector
Plasma
4kΩ
Gas line
Plasma gun installed at source chamber / Collector plate (295, Tungsten) installed at Expander
Gas injection : controlled by Piezo-electric valve (~ms response time)
Gas type : Ar / He
Both Plasma gun / Collector sustained by SUS pipe structure → Axial location adjustable
Power of the plasma source applied by Pulse forming Network (PFN) system
Plasma source / Collector

## Slide 10: Design of the pulsed plasma system
PFN power system
Pulse Forming Network (PFN)
Pulsed plasma needs long (~ms) moderate high voltage pulse to gun
Matching circuit / Load impedance, ladder-like connection → flat square pulse to load
PFN power bank system specification
Trigger system
Voltage for sustaining plasma is lower than initiating plasma discharge
Sudden (~100us) high voltage for breakdown → Sustain plasma with PFN power
Discharge power from trigger system → Sudden spark makes plasma column → Plasma discharged from PFN
PFN
Cathode
Cath-anode
Collector
PFN V / I simulation results
Trigger
Notes: R_load : 0.25 Ohm

## Slide 11: Initial plasma operation test
PFN power system
Time evolution of Gun Voltage / Current
PFN
Cathode
Cath-anode
R
Collector
PFN –Plasma gun circuit schematics
Condition : PFN Voltage 800V / Trigger voltage 1600V case
Max. ~350V / ~1.6kA, Voltage / Current is applied to gun → Plasma impedance ~ 0.22Ω (Not matched to expected 0.15Ω), Flat top : ~3ms (2~5ms)
Plasma gun power : maximum
Cause of waveform change : Internal resistance of inductor / Imperfect impedance matching / Stray Resistance
Gun current simulation considering
Flat top

## Slide 12: Initial plasma operation test
TLP measurement
Conditions
Magnetic field : (mirror region : 0.4T / center region : 0.078T)
TLP location : center chamber (-10cm from the center)
PFN : 800V / Trigger : 1600V
Base pressure ~3×10-7 Torr / Operating pressure ~ 1mTorr
Gas : Argon
Triple Langmuir Probe measurement result
Parameter averaged in Flat top (2~5ms)
  ~ / ~4.4eV
Preliminary measurement results, more analysis required to be confirmed
Flat top
Triple Langmuir Probe settings
Current measuring resistance : 10Ω / : 24V

## Slide 13: Initial plasma operation test
I-V curve / Ion saturation current measurement
Conditions
Magnetic field : (mirror region : 0.4T / center region : 0.078T)
TLP location : center chamber (-10cm from the center)
PFN : 800V / Trigger : 1600V
Base pressure ~3×10-7 Torr / Operating pressure ~ 1mTorr
Gas : Argon
Flat top
Measurement of I-V characteristic curve, saturation current
Discharge plasma by changing Biasing voltage ()
Measure current flowing at the probe tip for each shots
Extract current data at 2ms from the discharge, draw I-V curve
From the I-V curve,
Average ion saturation current at the Flat top (2~5ms) matches within ~25% from TLP data

## Slide 14
Summary / Future work
New pulsed linear magnetic mirror plasma device is constructed in KAIST
Research interests : Basic mirror plasma physics and fusion / industrial application
B field : center region 0.04~0.08T / mirror region 0.2~0.4T / Mirror ratio : 2.5 ~ 10
Plasma source : Arc plasma gun, ~350V / 1.6kA in initial experiments
Initial plasma parameter measurement : ne~6.9×1019m-3 / Te~4.4eV (by TLP)
Summary

## Slide 15
Summary / Future work
Future work
  Diagnose plasma characteristics from experiments of diverse condition
    Check reproducibility of the experiments by repeating same shots in many different timing
    Measure plasma parameter by changing location of Plasma gun and Collector
    Conduct electrode biasing in Collector and analyze the effect to the plasma parameter
    Measure plasma characteristics by changing PFN / Trigger voltage
    Study plasma parameter by changing magnetic field geometry configuration
  Improvement of KAIMIR plasma diagnostics
    Microwave interferometry – plasma line-integrated density
    OES measurement – Plasma radiation spectrum
    Diamagnetic loop – Plasma internal energy
    Probe measurement - Modification of physical model / data processing

## Slide 16
Thank you

## Slide 17: Backup slide
Magnetic coil specification
Mirror coil
Coil resistance : 1.026Ω / Inductance : 43.07mH / Number of turns : 360
Coil diameter: 278mm / weight : 15.1kg
Install location : ±730mm / ±645mm (From center)
L/R time (risetime) : 42ms
Solenoid coil
Coil resistance : 0.746Ω / Inductance 15mH / Number of turns : 120
Coil diameter : 620mm / weight : 10.9kg
Install location : ±388mm / ±138mm (From center)
L/R time (risetime) : 20ms

## Slide 18: Backup slide
PFN power system
PFN system
Sparker system
T1+
T1-
PFN-
PFN+
PFN power system circuit schematics

## Slide 19: Backup slide
CAD model of Plasma gun

## Slide 20: Backup slide
  Power balance equation Input Power – Power loss
  Assumption
    plasma volume as
    Stored energy
    Power efficiency of the gun to plasma ~ 50%
  ~300V, 1.2kA power will be applied to gun in ~5ms
  , choose where R : mirror ratio / : ion Coulomb collision time
  In steady state,
  Order is similar with experimental results
Power balance analysis

## Slide 21: Backup slide
Triple Langmuir probe design
10mm
100mm
200mm
Control box
DAQ
Circuit diagram
TLP Structure
2.2M
10 (Gain)
DC bias (24V)
Isolation amplifier
Tungsten tip
Triple Langmuir probe structure / circuit schematics
Triple Langmuir probe (TLP)
~5ms pulsed plasma diagnostics → high temporal resolution required
Utilize property of I-V characteristic curve of plasma from V / I value b/w probes, calculate plasma density / temperature
Directly measures plasma parameters without any voltage sweeping
Assume ideal I-V curve, measurement affected by DC bias and tip size
Probe / circuit design
Alumina tube : 100mm (Twice of predicted plasma radius)
Metal tip : 0.3, exposed length 10mm, Tungsten wire
Voltage measuring resistance : 2.2M (Make Floating tip current~0)
Current measuring resistance : 10 (better SNR, Saturation/voltage drop)
DC bias : 24V (Series connection of 12V lead-acid battery)
Measured data varies with DC bias value, Need cross-check with another diagnostics

## Slide 22: Backup slide
Operation procedure / timing
KAIMIR Nominal Operation procedure / timing settings
Base pressure ~3×10-7 Torr / Coil, PFN power bank charged
Piezo-electric valve is triggered → Operating pressure ~1mTorr
IGBT module of the coil is triggered
IGBT module of the PFN is triggered
Plasma is discharged from the PFN power
-200ms
0ms
200ms
-200ms ~ 100ms for both coil
-100ms ~ -50ms
Time line
0ms ~ 5ms
Plasma Discharge
B field generation
Gas injection